## Slide 1: Lumos The Smart Light Switch
Ari Biswas, Theo Dahlen, Jordan Friendshuh, Josh Graf

## Slide 2: Philips Hue
WiFi
110V AC

## Slide 3: Philips Hue
Smart Light App and light switch do not work together
WiFi
110V AC
Hue Bulb
Notes: If you turn off the light switch, you can no longer control the hue from your phone.
You shouldn’t have to think about how to go about turning on your lights. You should just do it.

## Slide 4: Philips Hue + Smart Switch
110V AC
Smart Switch
WiFi
WiFi
Hue Bulb

## Slide 5: Smart Switch + Conventional Bulbs
110V AC
Smart Switch
WiFi
IR
Standard or IR Bulb

## Slide 6: Contents
Why Lumos?
Hardware features
  Capabilities
  Power Board
  Top Board
Software features
  Tiva
  Peripherals
  Android App

## Slide 7: Hardware Features - Capabilities
Bulb Control
  WiFi
  IR LED
  Relay
User Input
  Knob
    Push Button
    Rotary Encoder
    RGB LEDs for Feedback
  Microphone
Enviroment Sensing
  Ambient Light Sensor
  Motion Sensor

## Slide 8: Hardware Features

## Slide 9: Hardware Features – Power Board
Input and Output Power Terminals
Relay
110VAC to 5V DC Power Supply
Compact Design
Notes: Explain the purpose of each component briefly. Actual usage covered in software section.

## Slide 10: Back of Power Board
Inter-Board Header
  5V, 3.3V, GND
  Relay controls
5V DC to 3.3V DC regular
Relay Control FETs

## Slide 11: Hardware Features – Top Board
TI CC3100 Wi-Fi
Illuminated rotary encoder with push button
IR LED
Ambient Light Sensor
Motion Detector
Microphone
Notes: Explain the purpose of each component briefly. Actual usage covered in software section.

## Slide 12: Hardware Features – Top Board (Back)
Tiva MCU
Microphone
Debug Header
  UART
  JTAG
Inter-Board Header

## Slide 13: Contents
Why Lumos?
Hardware features
  Capabilities
  Power Board
  Top Board
Software features
  Tiva
  Peripherals
  Android App

## Slide 14: Software Features - Tiva
Multithreaded, non-blocking networking C code
  Free RTOS
  CC3100 SDK
Code Structure
  Highly Modularized
Networking
  Manual HTTP JSON PUT requests
Notes: Explain how to use the board. What each component does. Describe software design? Demo while explaining?

## Slide 15: Software Features - IR
IR timer code
  PWM and time adjustment
NEC format
http://www.instructables.com/id/Reverse-Engineering-RGB-LED-Bulb-with-IR-remote/

## Slide 16: Software Features - Peripherals
Pushbutton Knob
Microphone
https://www.sparkfun.com/products/10596

## Slide 17: Software Features – Android App
Multithreaded sockets code
Android GUI
Android Async Task
Notes: Explain main features of android app. Demo while explaining?

## Slide 18
Questions?